## Slide 1: FROG 3.0
INSTALLATION SCHEMA

## Slide 2: Logical component location
Controller SDN (OpenDaylight)
Orchestastrator
OpenStack Controller
Virtual switches network
Compute Node
Virtual switches network
Network Node
Node
Controller

## Slide 3: Network infrastructure (Single Node)
Node
Controller
For simplicity both graphs and openstack control traffic exit by this eth
-
it has not its own IP address
Management eth.
Useful in case, for some reasons, a loop involved the vswitchs network
-
it has its own IP address
Control and Management eth
-
it has its own IP address
br-ex take its own IP address
br-int is the vswitch where all openstack vms are connected
L2 switch
br-usr
br-usr is the vswitch where all users are connected
L2 switch
br-int
L2 switch
br-ex
Controller SDN (OpenDaylight)
Orchestrator
L2 switch
br
Notes: Connection between br-ex and br-int are made from Orchestrator for every single graph.

## Slide 4: Router configuration

## Slide 5: UCS configuration
Compute/network node
This eth has no ip address configured
br-ex take its own IP address from dhcp or static
br-int is the vswitch where all openstack vms are connected
L2 switch
br-usr
br-usr is the vswitch where all users are connected
L2 switch
br-int
L2 switch
br-ex
ISR Router
ucse1/1
ucse1/0
eth0
eth1
eth2
This eth has no IP address configured